## Slide 1: Introduction to Reactive Transport with CrunchTope
Lawrence Berkeley National Laboratory
Carl Steefel
Christophe Tournassat
https://github.com/CISteefel/CrunchTope

## Slide 2
Acknowledgments
This work was supported by the Director, Office of Science, Basic Energy Sciences, Chemical Sciences, Geosciences, and Biosciences Division, of the U.S. Department of Energy under Contract No. DE-AC02-05CH11231 to Lawrence Berkeley National Laboratory.
Additional support was provided by the Center for Nanoscale Control of Geologic CO2, an Energy Frontier Research Center funded by the U.S. Department of Energy, Office of Science, Basic Energy Sciences.
This work was supported as part of the Watershed Function Science Focus Area at Lawrence Berkeley National Laboratory funded by the U.S. Department of Energy, Office of Science, Biological and Environmental Research.

## Slide 3
Latest Open Source CrunchTope
Latest CrunchTope Executables
https://github.com/CISteefel/CrunchTope
CrunchTope Release v2.0.1 (April 13, 2022)
https://github.com/CISteefel/CrunchTope/releases/tag/v2.0.1

## Slide 4: Closed versus Open Systems

## Slide 5: Characteristic Reaction and Transport Times
t = time
M = mass of solute
Q = volumetric flow rate
V = volume of reactor
C = concentration of solute
R = reaction rate
Conservation Equation
Steady State
Residence Time
Ratio of Characteristic Times

## Slide 6: Advective Transport
Concentration
Distance

## Slide 7: Diffusive Transport
Fick’s 1st Law
Diffusive flux is proportional to the concentration gradient
Fick’s 2nd Law

## Slide 8: Hydrodynamic Dispersion
Treatment of dispersive flux as a Fickian process
Dispersion coefficient
Does not capture the time dependence of the dispersion coefficient, which grows as the plume advances
Overestimates mixing and its effect on reactions

## Slide 9: Taylor-Aris Dispersion

## Slide 10: Macrodispersion
Velocity Field
Permeability Field
Flow Direction

## Slide 11: Macrodispersion
Flow Direction
Tracer Concentration Field
Comparison of 2D Heterogeneous Case and 1D Homogeneous Case
Capture
Plane

## Slide 12: Non-Dimensional Numbers Péclet and Damköhler
Péclet number
Damköhler I number
Damköhler II number
Non-dimensional form of advection-dispersion-reaction equation
Advection-dispersion-reaction equation

## Slide 13: Effect of Peclet Number

## Slide 14: Effect of Damköhler Number

## Slide 15: Analytical Solutions to ADR Equation
Solutions in one dimension for linear kinetics take the form
Pure advective transport
Pure diffusive transport
Mixed advective and diffusive transport

## Slide 16: Equilibration Length Scales
Equilibration length = λ

## Slide 17
Multicomponent Geochemistry

## Slide 18: Aqueous Speciation
Canonical Form
Primary Species
Secondary Species

## Slide 19: Total Concentration
Primary Species
Secondary Species

## Slide 20: Michaelis-Menten (Monod) Kinetics
E = electron acceptor
D = electron donor
Dual Monod
Inhibition Term

## Slide 21: Mineral Dissolution/Precipitation Rate Laws
General Form
Burch et al., 1993

## Slide 22: Cation Exchange
Exchange reaction involving Cs+ and a competing cation
Gaines-Thomas convention for activity of an exchange species
Selectivity Coefficient
Moles/g
Cation charge
Cation Exchange Capacity
Single exchange site
Multiple exchange sites

## Slide 23: Surface Complexation
Protonation-deprotonation reactions controlling surface charge
Electrostatic Effects
Surface charge density
First Acidity Constant
Second Acidity Constant

## Slide 24: Electrical Double Layer
Double Layers between Charged Surfaces
Solid line: Overlapping double layers
Dashed line: No opposite wall present
After Schoch et al, 2008

## Slide 25: Nernst-Planck Equation
Mobility
Fickian
Diffusion
Electrochemical
Migration
Activity Coefficient
Gradient
Electrostatic
Potential
Chemical Potential

## Slide 26: Nernst-Planck Equation
Left Boundary
pH 6.0
Cl- 0.1 mM
Na+ 0.1 mM
NO3- 0.001 mM
Initial Condition
pH 4.0
Cl- 0.1 mM
Na+ 0.1 mM
NO3- 0.1 mM
NOTE: No initial gradient in Na+ or Cl-, so Fick’s Law would say there is no diffusion

## Slide 27
Accumulation Term
Dispersion-Diffusion
Advection
Aqueous Reactions
Mineral Reactions
Gas Reactions
Fully Kinetic Approach
Partial Equilibrium Approach
Reactive Transport Equations
Total Concentration
Secondary Species
Rewritten with Primary Species

## Slide 28
Accumulation Term
Dispersion-Diffusion
Advection
Aqueous Reactions
Reactive Transport Equations: Numerical
Jx-1
Jx
Jx+1
Accumulation + Reaction Terms
Transport Terms
Rewrite Ψ in terms of primary species concentrations

## Slide 29: Short course exercises

## Slide 30
Introduction to speciation
Example using the carbonate system featuring various constraints
Stable isotopes of carbon (12C and 13C) implemented to demonstrate equilibrium fractionation
Advective transport
Introduce a non-reactive tracer into an advective flow field
Investigate numerical dispersion
Diffusive transport
Introduce a non-reactive tracer into a purely diffusive transport problem
No-flux versus Dirichlet boundary conditions
Multicomponent diffusion
Concept of charged species diffusing at different rates and electrochemical migration
Stable isotopes of Cl are implemented to consider the influence of diffusive fractionation
Transverse dispersion
Example based on a recent 2D dispersion experiment, including multi-ion diffusion in an advective flow field
Ion exchange
Introduce ion exchange of cesium in a 1D sediment column with competing Na+
Surface complexation
Surface complexation of zinc on iron-hydroxide (PHREEQc example 8)
CO2 attack on reservoir rocks
Diffusion of gas and flow of water, with variable liquid saturations and multi-mineral nucleation, precipitation, and dissolution
Calcite precipitation with isotopes
Simulation of stable isotope kinetic fractionation of calcium during carbonate precipitation
Two-dimensional flow fields
Xie et al (2015) benchmark on porosity and permeability change due to mineral reaction
Diffusion in clay
Tournassat & Steefel, 2016
Inverse modeling with PEST-CrunchFlow
Steefel et al, 2003
Short Course Exercises

## Slide 31: CrunchTope Files
Executable: CrunchTope.exe
Input file: name.in
Database(s): name.dbs

## Slide 32: CrunchTope Files
spatial_profile generated automatically at times specified (16, 32 hours)
OUTPUT
time_units hours
spatial_profile 16.0 32.0
time_series Rolle.out 11 20 1
time_series_print K+ Mg++ Cl-
time_series_interval 1
END/
time_series saved every time_series_interval in file Rolle.out
time_series_print writes species specified in file Rolle.out
Spatial profile files include:
  totcon#.tec total concentrations in solution
  pH#.tec solution pH
  conc#.tec log concentrations of individual species
  rate#.tec mineral reaction rates (mol/L(bulk)/s)
  aq_rate#.tec aqueous reaction rates (mol/L/s)
  volume#.tec mineral volume fraction (dimensionless)
  porosity#.tec (dimensionless)
  velocity#.tec Darcy flux (m3/m2/yr)
  toperatio_aq#.out per mil
  toperatio_min#.out per mil

## Slide 33
SPECIATION

## Slide 34: Exercise 1: Carbonate Speciation
Condition: speciate 1
Condition: speciate 2
Condition: speciate 3
Partial pressure CO2 fixed
Calculate pH for charge balance
Partial pressure CO2 fixed
Calculate pH for equilibrium with calcite
Partial pressure CO2 fixed
Calculate pH for alkalinity equivalence point

## Slide 35
Input Blocks
RUNTIME
speciate_only true
database_sweep false
database datacom_13C.dbs
graphics tecplot
density_module temperature
END
PRIMARY_SPECIES
H+
CO2(aq)
13CO2(aq)
Ca++
Na+
Cl-
END
SECONDARY_SPECIES
HCO3-
H13CO3-
CaCl+
CaCl2(aq)
CaOH+
HCl(aq)
NaCl(aq)
NaOH(aq)
OH-
CO3—
13CO3--
CaCO3(aq)
Ca13CO3(aq)
CaHCO3+
CaH13CO3+
NaCO3-
Na13CO3-
NaHCO3(aq)
NaH13CO3(aq)
END
GASES
CO2(g)
13CO2(g)
END
MINERALS
Calcite -label default -rate -11.00
END
Log rate (mol/m2/s)

## Slide 36
Stoichiometric Reaction Matrix

## Slide 37
Stoichiometric Reaction Matrix

## Slide 38
Condition speciate1
!! Fix pCO2 and calculate pH based on charge balance
units mol/kg
temperature 25.0
pH charge
!!gas partial pressure in bars
CO2(aq) CO2(g) 3.12E-04
13CO2(aq) 13CO2(g) 3.15E-06
Na+ 0.01
Cl- 0.01
Ca++ 0.00
END
Condition Blocks
Label for condition used in INITIAL_CONDITIONS and BOUNDARY_CONDITIONS and PUMP
Gas partial pressure in bars

## Slide 39
Condition Blocks
Condition speciate2
!! Fix pCO2 and calculate pH based on calcite equilibrium
units mol/kg
temperature 25.0
pH Calcite
!! Gas partial pressure in bars
CO2(aq) CO2(g) 3.12E-04
13CO2(aq) 13CO2(g) 3.15E-06
Na+ 0.01
Cl- charge
Ca++ 0.01
END

## Slide 40
Condition Blocks
Condition speciate3
!! Fix pCO2 and calculate pH based on alkalinity at the CO2
!! equivalence point (alkalinity = 0.00)
units mol/kg
temperature 25.0
H+ 0.00
!! gas partial pressure in bars
CO2(aq) CO2(g) 3.12E-04
13CO2(aq) 13CO2(g) 3.15E-06
Na+ 0.01
Cl- 0.01
Ca++ 0.00
END
Total Hydrogen = -Alkalinity

## Slide 41
DISCRETIZATION
xzones 1 1.0
END
INITIAL_CONDITIONS
speciate1 1-1
END
Discretization and
Initial and Boundary Conditions
NOTE: No boundary conditions needed for initial value problem
Minimum 3 grid cells required for a boundary value problem (with transport

## Slide 42: Exercise 1: Carbonate Speciation
View results in ShortCourse1.out

## Slide 43: Exercise 1: Carbonate Speciation with Isotopes
View results in ShortCourse1.out
δ13C = 0‰
δ13C = 4.6‰

## Slide 44
Speciation in ShortCourse1.out
From Speciate1

## Slide 45
ADVECTION

## Slide 46: Exercise 2: Advective Transport
distance
concentration
x = vt
Δx
L
Jx
Initial condition: junk2
Left boundary: junk1 flux
Right boundary: junk2 flux
For constant velocity and 1D
Courant-Friedrichs-Lewy Condition

## Slide 47: Numerical Dispersion
Upwind Scheme
Taylor Series Expansions
Even terms result in smearing and amplitude errors
Odd terms result in oscillatory phase errors
http://www.mathematik.uni-dortmund.de/~kuzmin/cfdintro/lecture10.pdf

## Slide 48: Numerical Dispersion
Exact Solution (Square Wave)
Upwind Finite Difference
Numerical dispersion

## Slide 49
Exercise 2 Procedure
Run CrunchTope in “GIMRT” mode, which uses 1st order upwind that introduces numerical dispersion
RUNTIME
time_units years
timestep_max 0.010
timestep_init 0.010
time_tolerance 0.1
hindmarsh true
master Tracer
database_sweep no
speciate_only false
gimrt true
database datacom.dbs
END
BOUNDARY_CONDITIONS
x_begin junk1 flux
x_end junk2 flux
END
INITIAL_CONDITIONS
junk2 1-100 1-1 1-1
END
DISCRETIZATION
distance_units meters
xzones 100 1.00
END
Condition junk1
units mol/kg
temperature 25.0
Tracer 0.1
END
Condition junk2
units mol/kg
temperature 25.0
Tracer 0.000001
END
FLOW
time_units years
distance_units meters
constant_flow 1.0
END
TRANSPORT
distance_units meters
time_units years
fix_diffusion 0.0
dispersivity 0.0
END
Boundary Condition
Initial Condition

## Slide 50
Exercise 2 Procedure
Run CrunchTope in “GIMRT” mode, which uses 1st order upwind that introduces numerical dispersion
Save “totcon1.out” as “totcon1_gimrt.out” to avoid being written over
Change to “gimrt false” so as to use TVD 3rd order accurate scheme with van Leer limiters
Rerun and compare “totcon1_gimrt.out” with “totcon1.out”
Now gradually increase dispersion in the input file (while still using OS3D mode (“gimrt false”) until you get a match between TVD (OS3D) profile and Upwind (GIMRT) profile
RUNTIME
time_units years
timestep_max 0.010
timestep_init 0.010
time_tolerance 0.1
hindmarsh true
master Tracer
database_sweep no
speciate_only false
gimrt false
database datacom.dbs
END
TRANSPORT
distance_units meters
time_units years
fix_diffusion 0.0
dispersivity 0.01
END
Gradually increase until you have a match
What dispersivity do you need to match?
Units of meters
Turns off upwinding, turns on higher order TVD scheme

## Slide 51
FICKIAN DIFFUSION

## Slide 52: Exercise 3: Fickian Diffusion
distance
concentration
Initial Condition

## Slide 53
TRANSPORT
distance_units meters
time_units second
fix_diffusion 1.E-09
dispersivity 0.0
END
DISCRETIZATION
xzones 501 0.0002
END
INITIAL_CONDITIONS
junk 1-501 1-1 1-1
boundary 251-251 1-1 1-1
END
Writes over earlier specified initial condition
Exercise 3: Fickian Diffusion
BOUNDARY_CONDITIONS
x_begin junk flux
x_end junk flux
END
“flux” uses flow rate through boundary, if flow rate = 0, then it becomes a No Flux BC
BOUNDARY_CONDITIONS
x_begin junk Dirichlet
x_end junk Dirichlet
END
After running “flux” BC, switch to “Dirichlet” (fixed concentration) and compare results
FLOW
time_units years
distance_units meters
constant_flow 0.0
END
Condition boundary
units mol/kg
temperature 25.0
Tracer 0.1
END
Condition junk
units mol/kg
temperature 25.0
Tracer 0.0001
END

## Slide 54: Exercise 3: Fickian Diffusion
Dirichlet boundary
Dirichlet boundary
Flux boundary
Flux boundary
NOTE: Error function analytical (ERF) solution only applies to infinite (or semi-infinite) boundary conditions, so would fail to describe system once mass reaches the boundary

## Slide 55
NERNST-PLANCK
MULTICOMPONENT DIFFUSION

## Slide 56: Exercise 4: Multicomponent Diffusion
Nernst-Planck Equation
Diffusion Potential
Flux from chemical potential
CrunchTope Equation
Fick’s Law
Diffusion Potential
Term vanishes if diffusion coefficients are all the same
Fickian
Electrical Potential
Activity Coefficient

## Slide 57
BOUNDARY_CONDITIONS
X_begin inlet Dirichlet
X_end initial flux
END
TRANSPORT
distance_units centimeters
time_units seconds
fix_diffusion 1.000e-05
formation_factor 1.0
cementation_exponent 1.0
D_25 H+ 9.312e-05
D_25 Na+ 1.334e-05
D_25 Cl- 2.032E-05
D_25 OH- 5.26e-05
D_25 NO3- 1.00e-05
END
Exercise 4: Multicomponent Diffusion
(with Nernst-Planck Equation)
Refers to Condition “inlet” and “initial”
Species-specific diffusion coefficients
NOTE: Hydrogen ion will try to diffuse faster than Cl- and Na+
TRANSPORT
D_25 H+ 1.000e-05
D_25 Na+ 1.000e-05
D_25 Cl- 1.000e-05
D_25 OH- 1.000e-05
D_25 NO3- 1.000e-05
END
Change diffusion coefficients all to same number and compare results
Condition initial
temperature 25.0
pH 4.0
Cl- 1.e-04
Na+ 1.e-04
NO3- 1.e-04
CO2(aq) CO2(g) 1.0E-16
END
Condition inlet
temperature 25.0
pH 6.0
Cl- 1.e-04
Na+ 1.e-04
NO3- 1.e-06
CO2(aq) CO2(g) 1.0E-16
END

## Slide 58: Exercise 4: Nernst-Planck Equation
Left Boundary
pH 6.0
NO3- 0.001 mM
Cl- 0.1 mM
Na+ 0.1 mM
Initial Condition
pH 4.0
NO3- 0.1 mM
Cl- 0.1 mM
Na+ 0.1 mM
NOTE: No initial gradient in Na+ or Cl-, so Fick’s Law would say there is no diffusion

## Slide 59
Left Boundary
pH 6.0
NO3- 0.001 mM
Cl- 0.1 mM
Na+ 0.1 mM
Initial Condition
pH 4.0
NO3- 0.1 mM
Cl- 0.1 mM
Na+ 0.1 mM

## Slide 60
TRANSPORT
distance_units centimeters
time_units seconds
fix_diffusion 1.000e-05
formation_factor 1.0
cementation_exponent 1.0
D_25 H+ 9.312e-05
D_25 Na+ 1.334e-05
D_25 Cl- 2.032E-05
D_25 37Cl- 2.028E-05
D_25 OH- 5.26e-05
D_25 NO3- 1.00e-05
END
ISOTOPES
primary 37Cl- Cl- 0.333
END
Rare Isotope
Common Isotope
Isotope ratio of standard
Exercise 4: Nernst-Planck with δ37Cl
Isotopic fractionation expressed in per mil
Note difference in diffusion coefficients (source of fractionation)
Find isotopic ratios in toperatio_aq1.out

## Slide 61: Exercise 4: Nernst-Planck with δ37Cl
Left Boundary
pH 6.0
Cl- 0.075
37Cl- 0.025
Na+ 0.1
NO3- 0.001
D_25 Cl- 2.032E-5
D_25 37Cl- 2.028E-5
Isotope Fractionation
Plot isotopic ratios in toperatio_aq1.out

## Slide 62
SORPTION

## Slide 63: Contaminant Retardation
Contaminant Velocity vc

## Slide 64: Exercise 6a: Cesium Ion Exchange
Exchange reaction involving Cs+ and a competing Na+
Gaines-Thomas convention for activity of an exchange species
Moles/g
Cation charge
Cation Exchange Capacity:
Single exchange site
Multiple exchange sites

## Slide 65: Real World Example for 137Cs Cation Exchange
Failure of Kd models spawned a major Science and Technology Program at Hanford funded by the U.S. DOE
Leaking high ionic strength waste tanks led to contamination of the deep Hanford Vadose Zone
Binary exchange data from Zachara et al. (2002)

## Slide 66: Cs Mobility in High Ionic Strength Solutions
Steefel et al., 2003; 2005
Greatest mobility of 137Cs was below the Hanford SX-108 tank
Competitive Effects on Radionuclide So
Cesium Kd in Hanford Sediments

## Slide 67: Exercise 6a: Cesium Ion Exchange
Input file
HanfordTank-A
HanfordTank-B
HanfordTank-C
NaNO3 injectate concentration
5 M
5 M
5 M
CsI injectate concentration
0
0.1 mM
0
Duration
19.25 hrs
125 hrs
Purpose
Precondition sediment
Active exchange of Cs for Na
Flushing sediment
76.5 hrs
Simulated sequence:

## Slide 68
RUNTIME
density_module sodium_nitrate
database HanfordTanksColumnFit3Site-GT.dbs
save_restart Column3NaNO3Flush1.rst
later_inputfiles HanfordTank-B.in HanfordTank-C.in
END
OUTPUT
time_units hours
spatial_profile 19.25
time_series Expt3ColumnFit.out 100
time_series_print Cs+ I-
time_series_output 0.00
END
BOUNDARY_CONDITIONS
x_begin nano3flush flux
x_end initial_condition flux
END
POROSITY
fix_porosity 0.405
porosity_update false
END
ION_EXCHANGE
exchange Xhan1-
exchange Xhan2-
exchange Xhan3-
convention Gaines-Thomas
END
DISCRETIZATION
distance_units centimeters
xzones 100 0.15228
END
Exercise 6a: Cesium Ion Exchange
Begin exchange
'NaXhan1' 2 1.0 'Na+' 1.0 'Xhan1-' 7.25224
'NaXhan2' 2 1.0 'Na+' 1.0 'Xhan2-' 4.93359
'NaXhan3' 2 1.0 'Na+' 1.0 'Xhan3-' 1.98868
'CsXhan1' 2 1.0 'Cs+' 1.0 'Xhan1-' 0.00
'CsXhan2' 2 1.0 'Cs+' 1.0 'Xhan2-' 0.00
'CsXhan3' 2 1.0 'Cs+' 1.0 'Xhan3-' 0.00
Database entries for log K (selectivity coefficients)
Assumes half-exchange reactions
Frayed edge site on illite
Planar sites on illite
3 types of exchange sites

## Slide 69
Condition initial_condition
units molar
temperature 25.0
pH 8.0
HCO3- CO2(g) 3.15e-04
K+ 0.0015
NO3- 0.001
Cs+ 0.000
I- 0.000
Na+ 0.001
Ca++ Calcite
Mg++ 0.00005
Tracer 0.0
Cl- charge
Xhan1- -cec 2.277023E-08
Xhan2- -cec 2.621486E-07
Xhan3- -cec 1.20E-04
Calcite 0.01 specific_surface_area 0.1
SolidDensity -ss_ratio 4698
END
Condition nano3flush
units molar
temperature 25.0
pH 8.0
HCO3- CO2(g) 3.15e-04
K+ 1.e-5
Cs+ 0.0
I- 0.0
Na+ 1.00
NO3- 1.00
Ca++ 0.0
Mg++ 0.0
Tracer 0.001
Cl- 0.0
Xhan1- -cec 2.277023E-08
Xhan2- -cec 2.621486E-07
Xhan3- -cec 1.20E-04
Calcite 0.01 specific_surface_area 0.1
SolidDensity -ss_ratio 4698
END
Initial Condition
Sodium Nitrate Flush
BOUNDARY_CONDITIONS
x_begin nano3flush flux
x_end initial_condition flux
END
Exercise 6a: Cesium Ion Exchange
Frayed edge site on illite
(eq/g)
Planar sites on illite (eq/g)
FLOW
time_units years
distance_units meters
constant_flow 638.2
END

## Slide 70
Condition cesiumflush
units molar
temperature 25.0
pH 8.0
HCO3- CO2(g) 3.15e-04
K+ 1.e-5
Cs+ 1.05e-4
I- 1.05e-4
Na+ 1.00
NO3- 1.00
Ca++ 0.000
Mg++ 0.0
Tracer 0.001
Cl- 0.0
Xhan1- -cec 2.277023E-08
Xhan2- -cec 2.621486E-07
Xhan3- -cec 1.20E-04
Calcite 0.01 specific_surface_area 0.1
SolidDensity -ss_ratio 4698
END
Cesium Spike: HanfordTank-B.in
BOUNDARY_CONDITIONS
x_begin cesiumflush flux
x_end initial_condition flux
END
Condition nano3flush
units molar
temperature 25.0
pH 8.0
HCO3- CO2(g) 3.15e-04
K+ 1.e-5
Cs+ 0.0
I- 0.0
Na+ 1.00
NO3- 1.00
Ca++ 0.0
Mg++ 0.0
Tracer 0.001
Cl- 0.0
Xhan1- -cec 2.277023E-08
Xhan2- -cec 2.621486E-07
Xhan3- -cec 1.20E-04
Calcite 0.01 specific_surface_area 0.1
SolidDensity -ss_ratio 4698
END
Sodium Nitrate Flush: HanfordTank-C.in
BOUNDARY_CONDITIONS
x_begin nano3flush flux
x_end initial_condition flux
END
Exercise 6a: Cesium Ion Exchange
This run “inherits” Cs contaminated sediment from HanfordTank-B run
This run “inherits” NaNO3 exchanged sediment from HanfordTank-A run

## Slide 71: Exercise 6a: Cesium Ion Exchange
Column
effluent breakthrough curve
Cs spike starts here
Cs spike stops here, only NaNO3 flush
Cs desorption

## Slide 72: Exercise 6b: Surface Complexation
Protonation-deprotonation reactions controlling surface charge
Electrostatic Effects
Surface charge density
First Acidity Constant
Second Acidity Constant
Surface Hydroxyl

## Slide 73: Exercise 6b: Surface Complexation
Surface Complexation of Zn+2 on Fe(OH)3
!!!Site name <site density mol/m**2>
>FeOH_weak 3.703704E-06
>FeOH_strong 9.259259E-08
Fe(OH)3 2.943109E-05 specific_surface_area 600.0
!!! Note: Gives 0.09 g/kgw water Fe(OH)3, 54 m**2 surface
Exercise will “sweep” the pH from 5.0 to 8.0 to show the Zn “pH edge”

## Slide 74
OUTPUT
time_units days
spatial_profile 365
time_series_at_node PHREEQCexample8.out 1 1 1
SURFACE_COMPLEXATION
>FeOH_strong on Fe(OH)3
>FeOH_weak on Fe(OH)3
END
Condition Solution1
temperature 25.0
pH 5.00
Zn++ 1.E-07 equilibrate_surface
Na+ charge
NO3- 1.0000E-01
Fe+++ 0.00
O2(aq) 2.4647E-04
!Site name <site density mol/m**2>
>FeOH_weak 3.703704E-06
>FeOH_strong 9.259259E-08
Fe(OH)3 2.943109E-05 specific_surface_area 600.0
SolidDensity 2600.0
!! Note: Gives 0.09 g/kgw water Fe(OH)3, 54 m**2 surface
!! Based on a density of 1017 kg/m**3, 1.017 g/cm**3
!! Volume Fraction Fe(OH)3 [m**3/m**3]*0.001*Molecular Weight Fe(OH)3/(Porosity*Molar Volume Fe(OH)3 [m**3/mole]) = g/L, but we want g/kg water, so g/L * (1/ro) = g/kgw
END
Partitions total concentration between surface and aqueous
Site densities for weak and strong sites
Exercise 6b: Surface Complexation

## Slide 75
CO2 ATTACK ON CEMENT

## Slide 76: Exercise 7: CO2 Attack on Cement
Dirichlet Boundary: Supercritical CO2 at 100 bars
No flux
Mineralogy:
Portlandite
Calcium-silica hydrate (CSH)
Calcite precipitates
Diffusion-Reaction System
Li, Steefel, & Jun, 2017

## Slide 77
Based on:
Li, Q., C.I. Steefel, Y-S Jun (2017) Deciphering calcium carbonate precipitation associated with CO2 attack on cement using reactive transport modeling. Environmental Science and Technology 51: 10861-10871, doi: 10.1021/acs.est.7b00594.
Exercise 7: CO2 Attack on Cement
Super-critical CO2
Cement

## Slide 78
Exercise 7: CO2 Attack on Cement
Li, Q., C.I. Steefel, Y-S Jun (2017) Deciphering calcium carbonate precipitation associated with CO2 attack on cement using reactive transport modeling. Environmental Science and Technology 51: 10861-10871, doi: 10.1021/acs.est.7b00594.

## Slide 79
RUNTIME
!!!fix_saturation 0.999
read_saturationfile QL_Saturation.dat
Duan true
Qingyun true
POROSITY
porosity_update true
minimum_porosity 0.015
porosity_exponent 3.00
porosity_threshold 0.017
END
Calcite -label nucleatecalcite
Calcite -label h+ -rate -3.0
Calcite_mix -label h+ -rate -3.0
SiO2(ammix) -label default -rate -6.5
SiO2(am) -label default -rate -6.5
SiO2(am) -label nucleateSiO2(am)
Portlandite -label default -rate -5.0
CSH(1.6) -label default -rate -7.8
CSH(0.8) -label default -rate -7.8
Bogusite -rate -35.00
Bogusite_i -rate -35.00
NUCLEATION
&Nucleation
NameMineral = Calcite
label = nucleatecalcite
A_zero25C = 0.00000001
B_nucleation = 0.000905
Sigma_mJm2 = 47
SSA_m2g = 1
Surface = Bogusite_i
/
END
NUCLEATION
&Nucleation
NameMineral = SiO2(am)
label = nucleateSiO2(am)
A_zero25C = 0.00000001
B_nucleation = 0.000905
Sigma_mJm2 = 20000
SSA_m2g = 1
Surface = Bogusite_i
/
END
Exercise 7: CO2 Attack on Cement
Two calcites with slightly different solubility
Pre-exponential J0
Constant terms
Interfacial free energy
Specific surface area of nucleated phase
Template for nucleation

## Slide 80
Condition Brine-Seed
!!Solution w/o minerals
temperature 95.0
units mol/kg
pH charge
CO2(aq) CO2(g) 100.0
Ca++ 0.0
SiO2(aq) 0.000001
SO4-- 0.0
Na+ 0.5
Cl- 0.50064
Calcite 0.0 ssa 1
Calcite_mix 0.0 ssa 1
SiO2(am) 0.0 ssa 1
SiO2(ammix) 0.0 ssa 1
CSH(1.6) 0.0
CSH(0.8) 0.0
Portlandite 0.0
Bogusite 0.0 0.0
Bogusite_i 0.01 ssa 1
set_porosity 16
!!set_saturation 0.95
Condition Cement
temperature 95.0
pH Portlandite
CO2(aq) 1.E-10
Ca++ 0.001
Na+ charge
Cl- 0.500
SiO2(aq) 0.0000001
Calcite_mix 0.00001 ssa 1
CSH(1.6) 0.31 ssa 1
CSH(0.8) 0.05 ssa 1
SiO2(ammix) 0.01 ssa 1
Portlandite 0.16 ssa 1
Bogusite 0.27 0.0
set_porosity 0.20
!!set_saturation 1
END
INITIAL_CONDITIONS
Brine 1-324
CO2 1-4
Brine-Seed 210-310
Cement 325-524
END
Exercise 7: CO2 Attack on Cement
DISCRETIZATION
distance_units microns
xzones 4 2000 320 100 200 10
END
Li et al, 2017

## Slide 81
Reactive Surface Area Options
Specific Surface Area (m2/g)
Condition Cement
temperature 95.0
pH Portlandite
CO2(aq) 1.E-10
Ca++ 0.001
Na+ charge
Cl- 0.500
SiO2(aq) 0.0000001
Calcite 0.00001 ssa 1
CSH(1.6) 0.35 ssa 1
SiO2(am) 0.10 ssa 1
Portlandite 0.20 ssa 0.01
Bogusite 0.20 1.0
Teflon 0.0 1.0
set_porosity 0.15
END
Bulk Surface Area (m2/m3)
Exercise 7: CO2 Attack on Cement
1.0000000e-01
1.0000000e-01
1.0000000e-01
1.0000000e-01
1.0000000e+00
1.0000000e+00
RUNTIME
time_units days
!!fix_saturation 0.999
read_saturationfile QL-saturation.dat
1st four grid cells are unsaturated (10%)

## Slide 82
Li et al, ES&T, 2017
Exercise 7: CO2 Attack on Cement

## Slide 83
ISOTOPIC FRACTIONATION

## Slide 84: Exercise 8: Calcite precipitation with δ44Ca
Solid
Fluid
Gebrehiwet et al., 2012
20 mm

## Slide 85: Exercise 8: Calcite precipitation with δ44Ca
Steefel et al. 2014
Isotope activities based on mole fractions

## Slide 86
INITIAL_CONDITIONS
amendment 1-1 1-1 1-1
END
DISCRETIZATION
distance_units centimeters
xzones 1 1.0
END
condition amendment
units mmol/kg
temperature 25.0
H+ 0.11544
Ca++ 5.28
Ca44++ 0.111997921
HCO3- 10.0
!! Mineral name <volume fraction m3/m3>
CalciteRifle 0.7833831 bsa 1.33E-02
Calcite44Rifle 0.0166170 bsa 1.33E-02
END
MINERALS
CalciteRifle -label default -rate -4.10000000
!!! 2 per mil kinetic fractionation
Calcite44Rifle -label default -rate -4.10217692
END
ISOTOPES
primary Ca44++ Ca++ 0.021667
mineral Calcite44Rifle CalciteRifle bulk
isotope_time_series BatchExperiment.out 1 1 1
END
Kinetic fractionation
Isotope Standard
Isotopic back-reaction with
Bulk
Surface
None
Exercise 8: Calcite precipitation with δ44Ca
Output isotope time series to file at grid cell

## Slide 87: Exercise 8: Calcite precipitation with δ44Ca
Steefel et al. 2014

## Slide 88: Exercise 8: Calcite precipitation with δ44Ca
δ44Ca (‰)
(1) Isotopically irreversible
fluid
bulk mineral
days
δ44Ca (‰)
(2) In equilibrium with bulk
fluid
bulk mineral
days
δ44Ca (‰)
(3) In equilibrium with surface
fluid
bulk mineral
days
Steefel et al. 2014
“None”
“Bulk”
“Surface”

## Slide 89: Exercise 9: Microbial Redox
E = electron acceptor
D = electron donor
Dual Monod
Druhan, Steefel, and others 2014

## Slide 90: Exercise 9: Microbial Redox
Rifle Sediment
CH3COO-(aq)
+ Rifle groundwater:
Uranium | 0.7 – 1.5 mM
pH | 7.0 – 7.2
Alkalinity | 7 – 10 meq/L
Eh | -150 to 240 mV
DO | 3 – 20 mM
Fe(II) | 15 – 50 mM
Nitrate | 2 – 3 mM
Sulfate | 8 – 11 mM
Sulfide | 0.03 – 0.5 mM
Acetate & Sulfate (mM)
Days
Fe++(aq) & HS- (μM)
Druhan et al., 2014

## Slide 91: Exercise 9: Microbial Redox
Druhan et al., 2014
Sulfate (mM)
Sulfate (mM)
10 cm
[SO42-]
δ34S
δ34S (‰)
Sulfate (mM)
δ34S (‰)
Sulfate (mM)
δ34S (‰)
δ34S (‰)
δ34S (‰)
Sulfate (mM)
50 cm
90 cm
day
day
day
70 cm
30 cm

## Slide 92
POROSITY-PERMEABILITY CHANGE

## Slide 93: Exercise 10: Porosity-Permeability
Xie, M., Mayer, K.U., Claret, F., Alt-Epping, P., Diederik, J., Steefel, C.I., Chiaberge, C., Simunek, J. (2015) Implementation and evaluation of permeability-porosity and tortuosity-porosity relationships linked to mineral dissolution-precipitation. Computational Geosciences 19: 655-671. DOI 10.1007/s10596-014-9458-3

## Slide 94
Condition mingliang_boundary
temperature 25.0
pH 3.0
Ca++ 0.0001
CO3-- 0.01
SO4-- 0.1
Fe++ 0.000223
!!Fe++ 8.0e-3
Fe+++ 0.0143
Al+++ 0.0143
K+ 7.67e-5
O2(aq) O2(g) 0.1005
Na+ 9.092e-2
Tracer 0.01
Calcite 0.30 1.00
Gypsum 0.00 1.00
Ferrihydrite 0.00 1.00
Jarosite 0.00 1.00
Gibbsite 0.05 1.00
Siderite 0.05 1.00
TracerMineral 0.35 1.00
END
Condition initial
temperature 25.0
pH 7.0
Ca++ charge
!!Ca++ 1.69512E-04
CO3-- CO2(g) 0.01
SO4-- 1.69512E-04
Fe++ 1.0e-5
Fe+++ 1.0e-10
Al+++ 1.0e-5
K+ 1.0e-5
O2(aq) O2(g) 1.E-15
Na+ 1.0e-15
Tracer 0.00001
Calcite 0.22 1.00
Gypsum 0.00 1.00
Ferrihydrite 0.00 1.00
Jarosite 0.00 1.00
Gibbsite 0.05 1.00
Siderite 0.05 1.00
TracerMineral 0.33 1.00
END
Exercise 10: Porosity-Permeability

## Slide 95
FLOW
distance_units meters
time_units second
calculate_flow true
read_PermeabilityFile perm5_2D.hyc SingleFile3D
!!IF homogeneous flow:
!!permeability_x 1.18602E-11 default
!!permeability_x 2.61491E-10 zone 0-0 1-40 1-1
!!permeability_x 2.61491E-10 zone 31-31 1-40 1-1
permeability_y 0.00 zone 1-31 42-42 1-1
permeability_y 0.00 zone 1-31 0-0 1-1
pressure 30 default
pressure 104.4365949 zone 0-0 1-41 1-1 fix
pressure 0.0 zone 32-32 1-41 1-1 fix
gravity 90.0 90.0 90.0
END
DISCRETIZATION
distance_units meters
xzones 1 0.050 29 0.10 1 0.050
yzones 1 0.025 39 0.05 1 0.025
END
MINERALS
!! Standard linear TST calcite
Calcite -label default -rate -4.301029996
Gypsum -label default -rate -4.301029996
Ferrihydrite -label default -rate -5.301029996
Jarosite -label default -rate -5.301029996
Gibbsite -label default -rate -6.301029996
Siderite -label default -rate -5.301029996
TracerMineral -label default -rate -35.00
END
Exercise 10: 2D Porosity-Permeability

## Slide 96: Exercise 10: 1D Porosity-Permeability
Xie et al, 2015

## Slide 97: Exercise 10: 2D Porosity-Permeability
Porosity update:
Permeability update:
Xie et al., 2015
Initial Permeability

## Slide 98: Exercise 10: 2D Porosity-Permeability
Xie et al., 2014
Calcite at 300 years

## Slide 99: Exercise 10: 2D Porosity-Permeability
Xie et al., 2015
Gypsum at 300 years

## Slide 100: Exercise 10: 2D Porosity-Permeability
Xie et al., 2015
Porosity at 300 years

## Slide 101
DIFFUSION IN CLAY

## Slide 102
Exercise 11: Diffusion in Clay
High concentration reservoir
Low concentration reservoir
Experimental setup

## Slide 103
Example of results
Data from Tachi & Yotsuji, 2014

## Slide 104
mol m-2 s-1
m s-1
Data from Tinnacher et al. GCA, 2016

## Slide 105
Geometry of the system, general properties
DISCRETIZATION
distance_units meters
xzones 1 0.0001 50 0.0001 1 0.0001
yzones 1 100
zzones 1 1
END
INITIAL_CONDITIONS
HReservoir 1-1 1-1 1-1
Clay 2-51 1-1 1-1
LReservoir 52-52 1-1 1-1
END
BOUNDARY_CONDITIONS
X_begin HReservoir Flux
X_end Lreservoir Flux
END
FLOW
space_units meters !!Default : meters ; km, cm, mm, um
time_units seconds !!Default : years ; days, hours, minutes, seconds
constant_flow 0.0 0.0 !!Default : 0.0
END
closed closed boundary conditions, only diffusion
Only one grid cell for the reservoir; large volume = 10 L

## Slide 106
Geometry of the system, general properties
POROSITY
fix_porosity 0.5
fix_microporosity 0.5
UpdateDDL false
MultiplyPorosityTortuosity true
END
New keywords that are specific to CrunchClay (ignored in CrunchTope)
TRANSPORT
distance_units meters
time_units second
fix_diffusion 1e-9
D_25 H+ 9.31e-9
D_25 Bogus 1e-20
D_25 OH- 5.27e-9
D_25 Na+ 1.3e-9
…
D_MP H+ 9.31e-9
D_MP Bogus 1e-20
D_MP OH- 5.27e-9
D_MP Na+ 1.3e-9
…
tortuosity 1 default
tortuosity 1 zone 1-1 1-1 1-1
tortuosity 0.037 zone 2-51 1-1 1-1
tortuosity 1 zone 52-52 1-1 1-1
tortuosityMP 1 default
tortuosityMP 1 zone 1-1 1-1 1-1
tortuosityMP 0.037 zone 2-51 1-1 1-1
tortuosityMP 1 zone 52-52 1-1 1-1
END

## Slide 107
Chemistry, surfaces, DL properties
Condition HReservoir
temperature 25.0
units mmol/kg
H2O 55.5
pH 7
Na+ 100
Cl- charge
Br- 1e0
Ca++ 1e0
Hto 1e0
Bogus Bogusite
Bogusite 3.1416e-8 specific_surface_area 750
>montmor- 1e-99 !!site per m2
set_porosity 0.999999999
set_microporosity 1e-10
END
Redefinition of the the bulk vs DL porosity for each of the domains
The reservoirs have a porosity value of 1
The surface charge is set to zero
Fake mineral with very low solubility that bears the surface
Background electrolyte concentration is high compared to the concentration of the tracers.

## Slide 108
Chemistry, surfaces, DL properties
Condition Clay
temperature 25.0
units mmol/kg
H2O 55.5
pH 7
Na+ 100
Cl- charge
Br- 1e-27
Ca++ 1e-27
Hto 1e-27
Bogus Bogusite
Bogusite 3.1416e-8 specific_surface_area 750
>montmor- 1.2e-99
set_porosity 5.655e-8
set_microporosity 5.0895e-7
END
Redefinition of the the bulk vs DL porosity for each of the domains
See explanation in input files for calculation of these values
Here bulk porosity is 10 % of the total porosity
The surface charge is set to zero
Fake mineral with very low solubility that bears the surface
Constant background electrolyte concentration

## Slide 109
Results
Concentration in the outlet reservoir
Why do the Br and HTO concentrations increase faster than the Ca concentration?

## Slide 110
Results
Increase the surface charge in the clay plug to 0.9 mol charge/kg clay
What is the species that diffuse the fastest now ?

## Slide 111
Results
Add surface complexation reactions:
>montmor- + Na+ = >montmorNa
2 >montmor- + Ca+2 = > >montmor2Ca
Begin surface complexation
'>montmorNa' 2 1.0 'Na+' 1.0 '>montmor-' -0.5 -0.5 -0.5 -0.5 -0.5 -0.5 -0.5 -0.5
'>montmor2Ca' 2 1.0 'Ca++' 2.0 '>montmor-' -1 -1 -1 -1 -1 -1 -1 -1
End of surface complexation
In database:
Begin surface complexation parameters
>montmor- -1.0
>montmorNa 0.0
>montmor2Ca 0.0
End surface complexation parameters

## Slide 112
Results
Add surface complexation reactions:
>montmor- + Na+ = >montmorNa
2 >montmor- + Ca+2 = > >montmor2Ca
The surface charge is partly compensated in the Stern layer (with no diffusion of sorbed species). The remaining charge is compensated in the diffuse layer
Total Charge in DDL (mol/m^3) = 5.6548800E-04
Total Fixed Charge (mol/m^3) = -5.6548800E-04
Microporosity = 1.470300000000000E-007
DonnanPotential = -9.386105664921650E-002
No surface complex
Total Charge in DDL (mol/m^3) = 2.8973120E-04
Total Fixed Charge (mol/m^3) = -2.8973120E-04
Microporosity = 1.470300000000000E-007
DonnanPotential = -7.672779885055225E-002
With surface complexes

## Slide 113
Results
Add surface complexation reactions:
What is the effect of Na and Ca surface complexation on Br and Ca diffusion?

## Slide 114
Summary

## Slide 115
INVERSE MODELING WITH PEST-CRUNCH

## Slide 116
Exercise 12: Inverse Modeling with PEST-CrunchTope
http://www.pesthomepage.org/Home.php
Use PEST together with CrunchTope for inverse modeling and sensitivity analysis
PEST

## Slide 117
pcf
* control data
restart estimation
4 165 1 0 1
1 1 double point 1 0 0
5.0 2.0 0.1 0.005 10
3.0 3.0 0.001
0.01
50 .005 4 4 .010 5
1 1 1
* group definitions and derivative data
all relative 0.01 0.0 switch 1.0 best_fit
* parameter data
k2a none relative 0.20000 -2.0 4.0 all 1.0 0. 1
k2b none relative 0.20000 -2.0 4.0 all 1.0 0. 1
k2c none relative 0.20000 -2.0 4.0 all 1.0 0. 1
k2d none relative 0.20000 -2.0 4.0 all 1.0 0. 1
BatchNoGmin.pst File
Number of parameters to be fitted
Number of observations
Parameters
* model command line
CrunchTope
* model input/output
datacom-SrExchange.tpl datacom-SrExchange.dbs
PestExchange.ins PestExchange.out
* observation groups
group_1
* observation data
SrCa-A11 0.00 1 group_1
SrCa-A12 0.00 1 group_1
SrCa-A13 0.00 1 group_1
SrCa-A14 42.37 1 group_1
SrCa-A15 0.05 1 group_1
SrCa-A21 1.19 1 group_1
SrCa-A22 0.56 1 group_1
SrCa-A23 0.37 1 group_1
SrCa-A24 40.50 1 group_1
SrCa-A25 0.00 1 group_1
Exercise 12: Inverse Modeling with PEST-CrunchFlow
Template file for PEST so it knows where to update parameters in CrunchTope input file
PEST instruction file
Generated by CrunchTope
At command line: i64pest BatchNoGmin.pst

## Slide 118
Datacom-SrExchange.tpl File
Tells PEST where to find the simulation data in PestExchange.out file to compare to observations
Primary Species uEquiv/kgw uEquiv/g solid
Ca++ 3.6555E+01 1.8278E-01
K+ 1.2860E+02 6.4298E-01
Mg++ 9.7581E+00 4.8791E-02
Sr++ 8.2991E+03 4.1495E+01
Na+ 6.0143E+00 3.0071E-02
Primary Species uEquiv/kgw uEquiv/g solid
Ca++ 2.2798E+02 1.1399E+00
K+ 2.0261E+02 1.0131E+00
Mg++ 9.6190E+00 4.8095E-02
Sr++ 8.0784E+03 4.0392E+01
Na+ 1.3673E+00 6.8364E-03
pif @
l2 [srca-a11]34:44
l1 [srca-a12]34:44
l1 [srca-a13]34:44
l1 [srca-a14]34:44
l1 [srca-a15]34:44
l2 [srca-a21]34:44
l1 [srca-a22]34:44
l1 [srca-a23]34:44
l1 [srca-a24]34:44
l1 [srca-a25]34:44
PestExchange.ins File
Generated by CrunchTope per instructions in BatchNoGmin.in file
'Sr-XB8814-2' 2 1.0 'Sr++' 2.0 'XB8814-2' 0.00 0.000
'Ca-XB8814-2' 2 1.0 'Ca++' 2.0 'XB8814-2' #k2a # 0.000
'Na-XB8814-2' 2 1.0 'Na+' 1.0 'XB8814-2' #k2b # 0.000
'Mg-XB8814-2' 2 1.0 'Mg++' 2.0 'XB8814-2' #k2c # 0.000
'K-XB8814-2' 2 1.0 'K+' 1.0 'XB8814-2' #k2d # 0.000
End of exchange
'Sr-XB8814-2' 2 1.0 'Sr++' 2.0 'XB8814-2' 0.00 0.000
'Ca-XB8814-2' 2 1.0 'Ca++' 2.0 'XB8814-2' .0918334263 0.000
'Na-XB8814-2' 2 1.0 'Na+' 1.0 'XB8814-2' -.909927443 0.000
'Mg-XB8814-2' 2 1.0 'Mg++' 2.0 'XB8814-2' .1465642933 0.000
'K-XB8814-2' 2 1.0 'K+' 1.0 'XB8814-2' -1.88939379 0.000
End of exchange
Exercise 12: Inverse Modeling with PEST-CrunchFlow
PestExchange.out File
Datacom-SrExchange.dbs File

## Slide 119
OPTIMISATION RESULTS
Parameters ----->
Parameter Estimated 95% percent confidence limits
value lower limit upper limit
k2a 9.183343E-02 8.310404E-02 0.100563
k2b -0.909927 -1.47566 -0.344194
k2c 0.146564 0.127452 0.165677
k2d -1.88939 -1.96078 -1.81801
Note: confidence limits provide only an indication of parameter uncertainty.
They rely on a linearity assumption which may not extend as far in
parameter space as the confidence limits themselves - see PEST manual.
See file batchnogmin.sen for parameter sensitivities.
Observation Measured Calculated Residual Weight
value value
srca-a11 0.00000 0.182780 -0.182780 1.000
srca-a12 0.00000 0.642980 -0.642980 1.000
srca-a13 0.00000 4.879100E-02 -4.879100E-02 1.000
srca-a14 42.3700 41.4950 0.875000 1.000
srca-a15 5.000000E-02 3.007100E-02 1.992900E-02 1.000
srca-a21 1.19000 1.13990 5.010000E-02 1.000
srca-a22 0.560000 1.01310 -0.453100 1.000
srca-a23 0.370000 4.809500E-02 0.321905 1.000
srca-a24 40.5000 40.3920 0.108000 1.000
srca-a25 0.00000 6.836400E-03 -6.836400E-03 1.000
BatchNoGmin.rec File
Exercise 12: Inverse Modeling with PEST-CrunchFlow
Find summary of optimization results in *.rec file generated by PEST

## Slide 120
Numerical Approach

## Slide 121
The derivative of the total concentration with respect to the primary species concentrations
Or using the logarithms of the concentrations as the primary unknowns (which scales the Jacobian matrix, making it numerically more tractable)
Derivative of Total Concentration

## Slide 122
Jx
Jx-1
Jx+1
Jacobian Matrix for Global Implicit Method
Jx-1
Jx
Jx+1

## Slide 123
Newton’s Method for Global Implicit Method
Nc x Nc Jacobian Submatrix
Nc Residual Vectors

## Slide 124
Newton’s Method for Global Implicit
For JX = 2
Nc x Nc
Nc x Nc
Nc x Nc